## Slide 1: Intro to fpga
Mateusz wolak

## Slide 2: Software vs hardware design
Software
The development and testing of programs/code
Instructions given to a computer, which is interpreted into physical signals
Think: loops and classes
hardware
The development and testing of physical computer systems
The design of the actual physical hardware software runs on, ie. processors
Think: logic gates and integrated circuits

## Slide 3: What is fpga?
Stands for field-programmable gate array
  Comes from the fact that they can be reprogrammed “in the field”
FPGAs are pieces of re-configurable computer hardware
You specify a circuit, and the FPGA is configured to match that design – this can be as simple as 1 logic gate, or as complex as entire multicore processors
Produced by 4 major vendors: Xilinx, Altera (intel), Lattice, and Efinix
Can cost anywhere from $1 to $91,000

## Slide 4: Basic architecture
Programmable logic blocks – implement basic logic functions
  Combinatorial logic - and, or, xor …
  Flip-flops – store output from combinatorial logic
  Specialized blocks (ie. memory) – vendor specific
Programmable interconnects – link logic blocks together as specified
Programmable I/O – make off-chip connections

## Slide 5: Workflow - Programming
FPGA
Designs are specified using HDLs (hardware description languages), such as Verilog and VHDL
Software
Designs are specified with high-level programming languages, such as C++, Java, and Python

## Slide 6: Workflow - compilation
FPGA Steps
Synthesis – Verilog is converted into a netlist, which describes the basic blocks (primitives) needed (think a recipe)
Place & Route (P&R) – Netlist is mapped to the primitives physically present on the FPGA (matching to the ingredients you have)
Bitstream generation – Results of P&R are translated into a format the FPGA can read from flash memory (hex)
Software Steps
Compiler – High-level programming language is converted into instructions the processor understands. (example: GNU compiler for C++)
Linker – combines the various compiled files in a project into one executable to run on the processor
Executable – .exe

## Slide 7: Workflow - Debugging
FPGA
Debugging is done by looking at waveforms (physical signals)
Software
Debugging is done by looking at data values (software constructs)

## Slide 8: In the real world
Strengths
Parallel processing – circuits on an FPGA can work completely independent of one another, greatly accelerating certain workloads
Reconfigurable – can be reprogrammed to a completely different hardware configuration quickly.
Configurable IO – easy to connect and swap various peripherals
weaknesses
Less space and energy efficient – because they are reconfigurable, they contain many elements you don’t use, eating up space and power
Low clock speed – generally, fast FPGAs clock in around 500 MHz, where current CPUS are pushing 5 GHz, not ideal for naturally sequential tasks
applications
Used to design, prototype and test ASICS before and early in mass production
Overlap with ASIC - Image processing, DSP, aerospace & defense, medical systems, etc.
Reconfigurability makes it perfect for certain tasks – Microsoft is using FPGAs to run Bing search algorithms, so that they can be reconfigured as algorithms change
Notes: Flexible IO

## Slide 9: Fpga Board Examples
Fireant
The FPGA development board we will use in this workshop
Uses an Efinix Trion T8 FPGA (7k LE, 123Kb RAM)
Low-power and simple, making it perfect for getting started with FPGA
Low cost - $38 on Crowd Supply
Easy to use IDE for development
Darsena (mind chasers)
Uses Lattice ECP5-UM FPGA (44k LUT, 1944 Kb RAM)
Large and powerful chip, enabling advanced functionality (private island project)
Integrated ethernet PHYs, with 4-channel PCS/SERDES on the FPGA
Powerful IDE for development

## Slide 10: Verilog HDL
Used to design a hardware configuration to be put onto the FPGA
HDL = hardware description language, NOT a programming language
With Verilog, don’t think of it in terms of coding – instead, you are specifying a hardware layout.

## Slide 11: Basics
module – basic Verilog construct used to house logic. Has inputs & outputs, connecting them as specified by the logic.
assign – keyword used to connect elements in Verilog. The connection it describes is continuous.

## Slide 12: Basic example
module top_module (input btn1, input btn2, output led1, output led2);
assign led1 = btn1;
assign led2 = btn2;
endmodule;
Notes: Show programming of board and click the buttons & stuff on webcam

## Slide 13: wire
Basic type in Verilog, symbolizes a wire (shocking) used to connect different elements w/ continuous assignment
In our previous example, the inputs and outputs were all implicitly type wire
Can also be declared explicitly to connect logic inside of a module like this:
wire w;
assign w = a
assign b = w

## Slide 14: Operators
~ = NOT
& = AND
| = OR
^ = XOR
Applied to elements in expressions like so:
  in1 & in2
  in1 & ~in2 | in3
  Etc.

## Slide 15: Practice
Task: create the circuit shown on the left using Verilog HDL.
Design:
led1 driven by AND operation of btn1 and btn2
Led2 driven by OR operation of btn1 and btn2
Notes: Have them write the Verilog for this on their own

## Slide 16: Solution
module top_module (input btn1, input btn2, output led1, output led2);
assign led1 = btn1 & btn2;
assign led2 = btn1 | btn2;
endmodule;
Notes: If small group – have each person deploy to board and interact with the buttons – then show Verilog  bitstream
If large group – have each person compare their code, then go through and show everyone full process Verilog  bitstream and let them interact with the buttons

## Slide 17: clock
External signal, generated by an oscillator
Used to synchronize the components in a circuit – synchronous computing
Generally, all operations happen on the rising edge

## Slide 18: Binary values
Numbers represented in base 2, rather than base 10
Each place is called a “bit”
Each place represents a power of 2, with the right being lowest
  2^3, 2^2, 2^1, 2^0
  1011  11
Verilog syntax: 4’b11

## Slide 19: register
Basic element used to store information
Holds its value until the next rising edge of the clock
In Verilog:
  Uses “reg” keyword
  Has a defined size, and stores a binary value
  Syntax:
reg [15:0] reg_name = 16'b0;

## Slide 20: Type groups
Two groups of types in Verilog
“Nets” are types for connecting components  continuous assignment
  Wire belongs to this group
“Variables” are types for storing information  synced with clock
  Reg belongs to this group
Notes: Here, do 3-bit register counting example on the board

## Slide 21: Always block
Container for defining synchronous logic within a module
“<=“ used for assignment
Everything inside must be “variable” type
Uses “always”, “posedge”, “begin” and “end” keywords
Syntax:
always @ (posedge clk) begin
a <= b;
end

## Slide 22: Clock example
module top_module (input clk, output led1, output led2);
reg [15:0] clk_count = 16'b0;
assign led1 = (clk_count[15] & clk_count[14]);
assign led2 = ~(clk_count[15] & clk_count[14]);
always @ (posedge clk) begin
clk_count <= clk_count + 16'b1;
end
endmodule
Notes: Again, show this on the board

## Slide 23: Side note
Technically, the way we used the clock was incorrect
On power-up, the oscillator produces an unstable clock, and we don’t want to be performing any operations at this time
This is overcome with something called pll, which produces a signal when the clock is stable – we use this to delay operations
Additionally, our board should use a reset button – so that the contents of the register are in a known state

## Slide 24: Proper example
module top_module (input pll_LOCKED, input pll_CLK, input btn1, output led1, output led2);
reg [25:0] clk_count;
assign led1 = (clk_count[25] & clk_count[24]);
assign led2 = ~(clk_count[25] & clk_count[24]);
always @ (posedge pll_CLK, negedge btn1) begin
if(btn1) begin
clk_count <= 26'b0;
end
else if (pll_LOCKED) begin
clk_count <= clk_count + 26'b1;
end
end
endmodule
Notes: Again, show this on the board

## Slide 25: Demo
Notes: Tell people how to get started